## Slide 1: Slow walking velocity of an adult human
The slow, normal walking speed of an adult human is around 3,5km/h.
Slow walking speed | 3,5km/h
Step length at 3,5km/h around | 70cm
Steps per hour (with 70cm) | 5000
Time to take a single step (70cm) | 0,72s
Feet distance while standing | 30cm
In other words To take one full step (70cm) in 0,72s, the axis has to rotate from 0° to +66,8°. This makes around 92,8° per second or 15,5rpm where the disc has to spin. Note: 15,5rpm is not the fastest speed which has to be achieved, because the rotation speed depends on tangens and the feet distance (while standing).
-35
35
-10
-20
10
20
66,8°
70cm
30cm

## Slide 2: Walking straight ahead with 70cm in 0,72s
Chart: 
RPM | 30.4028 | 27.5066 | 23.0906 | 18.595 | 14.7538 | 11.7213 | 9.4001 | 7.6348 | 6.2853 | 5.2425 | -5.2425 | -6.2853 | -7.6348 | -9.4001 | -11.7213 | -14.7538 | -18.595 | -23.0906 | -27.5066 | -30.4028 | -30.4028 | -27.5066 | -23.0906 | -18.595 | -14.7538 | -11.7213 | -9.4001 | -7.6348 | -6.2853 | -5.2425 | 5.2425 | 6.2853 | 7.6348 | 9.4001 | 11.7213 | 14.7538 | 18.595 | 23.0906 | 27.5066 | 30.4028
Note: as you can see, the highest rpm is about 30rpm or 180°/second.